Managing Flood Hazard Identification in Alberta

J. Choles, C. Mahabir1, B. Haimila1, and P. Stevenson1

River Engineering Team, Alberta Environment.

Abstract:  Flood hazard identification forms the foundation of any strategy to manage the risk associated with floods by defining the area of concern. Alberta has been producing flood hazard mapping studies since the early 1970’s.  The flood hazard studies were initially provided to communities as information to support development planning.  After signing the Flood Damage Reduction Program (FDRP) agreement with the federal government in 1989, the process was formalized through designation by the various levels of government.    Since the termination of the FDRP agreement in 1999, designation has proceeded under the provincial Water Act and flood hazard identification has continued as a provincial program.

Many communities across Alberta have completed flood hazard identification studies.  This information is available in a variety of ways including a GIS based website.  Every year additional flood hazard studies are completed for vulnerable communities across Alberta.  After each major flood event, data is collected specifically to support future studies and updates to existing studies.

Flood hazard identification mapping is a useful tool for reducing flood damages but it has its limitations and does not address all potential flooding issues.  Selection of a design flood can be complicated, especially when flows are regulated by a dam or series of dams upstream or if ice jams are a potential concern.

This paper presents the history of flood hazard identification in Alberta, challenges in defining the flood risk area, policies related to dykes, accuracy issues, local acceptance, the responsibilities of the various levels of government and methods of conveying flood information,.  Despite its limitations, flood hazard identification has resulted in increased public safety and reduced flood damages in Alberta.

Key Words: flood hazard, flood risk

# Introduction

Flooding is a problem in Alberta.  Over the past 15 years, there was major flooding in High River, Pincher Creek, Lethbridge and Medicine Hat and area (1995), Fort McMurray and Peace River were flooded by ice jams (1997), and High River, Okotoks, Calgary, Sundre, Rocky Mountain House, Red Deer and Drumheller and area suffered severe flooding (2005).  Flooding represents one of the largest expenses for Disaster Financial Assistance.  For example, the 2005 flood resulted in over $165 million in Disaster Financial Assistance payments and four deaths.

To assist Albertans in reducing flood losses, Alberta Environment supervises the production of flood hazard mapping studies for flood prone areas.  Flood hazard mapping studies are undertaken to define the flood hazard for the design flood for a community. This information can then be used by local governments when making development and planning decisions.

In this article, flooding is defined as overland flow from a water body such as a river or lake caused by excessive flow or an ice jam.  Flooding caused by drainage problems, storm water, structural failures or water table problems is not addressed.

# history

Alberta has produced flood hazard mapping studies since the 1970’s.  In 1989 Alberta signed “An Agreement Respecting Flood Damage Reduction and Flood Risk Mapping in Alberta” (FDRP) with the federal government to cost share flood hazard identification studies among other efforts to increase public safety and awareness to reduce flood damages.  A list of 66 communities requiring flood hazard identification studies was drawn up as part of that agreement.  The agreement was terminated in 1999 without completing flood hazard identification studies for all the communities on the list.  Since then, Alberta Environment has continued to produce flood hazard identification studies for the remaining communities on the list.  As of March 31, 2008, 46 studies have been completed.

Since the FDRP agreement has been terminated for several years, Alberta Environment decided to review the flood hazard program to produce new guidelines.  It was also an opportunity to compile policies and review the standard operating procedures that had been used.

# defining the flood hazard area

The simplest way of avoiding flood damages is to not have flood vulnerable development in flood prone areas.  The first step in this process is to identify the area of concern.  The flood hazard area is the area of land that will be flooded during the design flood event.  Once this area is defined, the flood hazard area is typically divided into two zones, the floodway and the flood fringe.  In some circumstances, where there is not enough information to delineate two zones, one zone mapping will be created where, for development purposes, the entire flood hazard area is treated as floodway.  Figure 1 shows the flood hazard area for a typical community with the floodway and flood fringe zones defined.

The floodway is defined as the area within which the entire design flood can be conveyed while meeting certain water elevation rise, water velocity and water depth criteria.  The floodway typically includes areas where the water is 1 metre deep or greater, the local velocities are 1 m/s or faster or if the river were encroached, the water level rise would be 0.3 m or more.

The flood fringe is that part of the flood hazard area that has relatively shallow water (less than 1 metre deep) with lower velocities (less than 1 m/s) under encroached conditions.  Technically it is that part of the flood hazard area that is not included in the floodway.  The final flood elevations on the flood hazard maps assume that the entire flood fringe has been filled in and all the flow is conveyed by the floodway (Figure 1).  This is a forward looking assumption that considers the possibility that development will eventually fill in the entire flood fringe, as permitted in the guidelines.

Figure 1:  Aerial view of a typical 2-zone flood hazard area divided into the floodway and flood fringe (based on CAFDRP, 1989).

# Data Collected to Support Flood Hazard Maps

Various data are collected to calibrate and check the hydraulic models used to delineate the flood hazard area.  These data document historic flood events that are used to calibrate the hydraulic model.  Being able to verify a hydraulic model increases our confidence in the final results.

## High-water Mark Information

High-water marks refer to evidence denoting the maximum water elevations at a specific location for a particular river flow of interest.  Alberta Environment surveys high-water marks after significant flood events along reaches of interest.  Local governments, residents, railways and Alberta Infrastructure and Transportation are also potential sources of high-water mark data.  High-water marks are used to calibrate the hydraulic model.

## Aerial Photography

Aerial flood photographs may be ordered by the province whenever a significant flood event occurs.  They provide an historical record of past floods and can be used to calibrate the hydraulic model.  Currently Alberta Environment arranges for aerial flood photography and Alberta Sustainable Resource Development is the custodian of aerial photos.

## Rating Curves

If there are gauging stations in the reach being studied, the rating curves can also be used in model calibration.  The gauging stations record water levels that are converted to discharges using the rating curves.  Rating curves show the relationship between the water surface elevation and the discharge, based on measurements taken at the gauge (Figure 2).  By comparing historic rating curves, the relative stability of a reach can be evaluated.

Figure 2:  Historic rating curves for the Red Deer River at Red Deer for the period January 1, 1998 to 2007.  Note the natural variation between the rating curves.

## Historic Information

Historic newspaper articles, photos and personal recollections can provide useful information on historic floods.  Usually they are used to confirm how large an historic flood was.  Sometimes individuals can remember how high the water rose during an historic flood at certain locations and this information can be used to help calibrate the flood model.

# design flood

The flood event used to delineate the flood hazard map is called the design flood.  The design flood is a flood that may occur in any year, due to open water or ice jam flooding, with a certain probability of occurrence or exceedence. The chosen flood allows for the estimation of the risk of a certain location being flooded.  There are larger, less frequent floods and smaller, more frequent floods.  The design flood is chosen to balance the risk of flooding with the desire for development. Alberta’s Flood Hazard Identification Program uses the 1:100 year return period open water flood (the flood that has a one per cent chance of being equalled or exceeded in any one year) or the 1:100 year return period ice jam water elevation, if an ice jam is used as the design event, as the standard benchmark for flood management policies.  A flood with a 100 year return period is also referred to as the 1:100 year flood and as being a 1:100 frequency event.  Once a discharge or elevation is chosen, it is then referred to as the design discharge or design elevation for the flood hazard identification study.  Other provinces have used other floods as the design flood.  A summary of the standards used across Canada under the FDRP is summarized in Table 1.  Table 1 shows that while there was some variation in the design flood and floodway definitions, the standards were fairly consistent across Canada.

As discussed in the previous paragraph, for most buildings in Alberta, the minimum flood hazard is the 1:100 year return period flood.  However, for public facilities that perform a function of significant importance to the health, safety and welfare of a community, a lower level of risk may be appropriate.  For public facilities that are considered to be “Lifelines,” facilities that perform a function of significant importance to the health, safety and welfare of a community, a lower level of risk is warranted.  Lifeline Structures, such as administration buildings, essential roads etc. are recommended to have at least a 1:500 year return period (0.2 per cent probability of annual occurrence) level of flood protection. Vital Lifeline Structures, such as hospitals, are recommended to have a 1:1000 return period year (0.1 per cent probability of annual occurrence) level of flood protection.  Following these standards will increase the likelihood that, during a serious flood event, vital infrastructure will still be able to operate (Alberta Infrastructure, 2001).

Table1:  Definitions of regulatory floods and floodways for various Canadian jurisdictions during the Flood Damage Reduction Program.

| Province/Territory | Regulatory Flood Return Period | Definition of Floodway |
| --- | --- | --- |
| B.C. | 1:200 | the natural channel plus a minimum 30 m setback. |
| Alberta | 1:100 | Hydraulic1 |
| Saskatchewan | 1:500 | Hydraulic1 |
| Manitoba | 1:100 | Hydraulic1 |
| Ontario | 1:1002 | 1:100 |
| Quebec | 1:100 | 1:20 |
| New Brunswick. | 1:1003 | 1:20 |
| Nova Scotia | 1:1003 | 1:20 |
| P.E.I. | 1:1003 | 1:20 |
| Newfoundland and Labrador | 1:1003 | 1:20 |
| N.W.T | 1:100 | Hydraulic1 |
| Nunavut | 1:100 | Hydraulic1 |

Notes:

- The hydraulic criteria uses 1 m depth, 1m/s velocity or 0.3 m water level rise

- Ontario uses the Hurricane Hazel rainfall, the Timmins storm and the 1:100 elsewhere

- The Atlantic provinces may also use a historic event provided the water levels are higher than the 1:100 flood

In Alberta the design flood magnitude is usually based on natural flows.  Dams in the province are typically operated for flow augmentation or hydroelectric power generation purposes.  These objectives are not consistent with flood control as the reservoirs would usually be managed to meet their primary objectives and to ensure the safety of the structures.  During a flood event, the provincially operated dams will be operated to dampen the flood peaks if possible, but unless they have dedicated flood storage, it is not possible to predict what effect they will have on flood flows for planning purposes.

# dykes

Dykes are barriers constructed to prevent surface water from rivers or lakes from flooding surrounding lands.  Often dykes are earth berms but they can also be constructed of concrete and other materials. In Alberta’s program, any dyking present is generally assumed to be ineffective and the flooded area behind the dyke would be considered floodway or flood fringe.  This is a conservative assumption but it reflects the potential flood hazard if the dykes were to fail.  Alberta Environment’s policy has been that dykes are constructed to protect existing development and not to create development opportunities on vacant flood prone land.  Consequently it is recommended that any new development constructed behind a dyke should also be floodproofed.  It should be noted that although dykes may prevent surface waters from causing flood damages, the water table will still rise in response to river or lake levels.  This rise in the water table may result in basements and other underground structures being flooded.

# DEsignation

Designation is the formal acknowledgement of the flood hazard area by the local and provincial governments.  It also marks the official commencement of any policies related to flood management within the flood hazard area by the provincial government.  Under the Water Act, proclaimed on January 1, 1999, the Minister of the Environment may designate a flood hazard area and specify acceptable land uses within the flood hazard area.  Section 96 of the Water Act describes this power to designate a flood hazard area, subject to the regulations.  Once an area is designated as a flood hazard area the local government is expected to take the flood hazard into account when approving development, zoning or writing bylaws.

Under the Flood Damage Reduction Program (1989 to 1999), designations were made with both the federal and provincial ministers for the Environment authorizing the designation.  These designations had the same purpose as the present provincial ones and they are recognized by the present program.

## Implications of Designation of a Flood Hazard Area

Designation is a formal term used by the provincial government that accomplishes two purposes:

- It documents the acceptance by all levels of government of the areal extent of the flood hazard area; and

- It signals the initiation of specific actions and policies by the provincial and municipal governments.

After a flood hazard area is designated the provincial government:

- will ensure that provincial departments and agencies will not construct any developments in the designated flood hazard area that are vulnerable to flood damage;

- will ensure that provincial departments and agencies do not cost share any developments in the designated flood hazard area that are vulnerable to flood damage;

- will encourage the local authorities to impose land use restrictions that prohibit development vulnerable to flood damage within a designated flood hazard area or, where appropriate, make such development subject to floodproofing requirements; and

- may restrict disaster recovery compensation programs such that no funding is available for costs or losses incurred as the result of a flood within any designated flood hazard area if the development was initiated after the date of designation, unless such a development was adequately floodproofed.

The municipality, as the responsible agency for regulating development within its area of jurisdiction, is charged with ensuring that new development conforms to the zoning and development guidelines.  Conformity to the development guidelines will minimize future flood damages and thus future disaster recovery compensation payments and increase public safety.  As of 2008, the Minister of Environment has not used his authority to determine land use within a local government’s jurisdiction, as it is assumed that the local governments will make responsible decisions.

# Frequently asked questions

When flood hazard studies are produced, there are sometimes questions or objections to them.  Three issues that have commonly arisen in the past are the impact of the maps on land values, the accuracy of the flood hazard mapping and elevations and the definition of a 1:100 year flood event.

## Property Values

One concern that sometimes arises is that the flood hazard map may cause devaluation of the lands that are identified as flood prone as potential buyers may see them as less desirable.  Affected landowners sometimes feel that they should be compensated for this perceived drop in value.  However, the flood hazard maps simply identify an existing risk, that is present whether it is recognized or not.

## Accuracy

There are two issues in terms of accuracy, the accuracy of the calculated water elevations and the accuracy of the location of the flood lines on the maps.

Generally the calculated water elevations associated with flood hazard mapping are considered to be accurate within 0.5 m or less.  When floodproofing a structure it is recommended that a freeboard is added to the elevation to provide an additional element of security.  The freeboard accounts for uncertainties introduced as part of the hydraulic modelling, changes in the river channel (see Figure 2) and land settlement.  The recommended free board is 0.5 metres.

The floodlines on the flood hazard maps have a planning level of accuracy.  The lines are drawn where the calculated water surface intersects the ground surface represented on the map.  Given that the maps to delineate flood lines generally have an accuracy of plus or minus half a contour interval, 90% of the time, trying to locate the flood line to the nearest millimetre is not appropriate.  A ground survey will give a much better approximation of the flood line on a property. It is also important to note that beyond the flood line, the water table may rise in response to flood levels in a river or lake.  Consideration should be given to restricting development below the design flood elevation to avoid water table problems associated with the river or lake level.

## 1:100 year Flood

The design flood for Alberta is the 1:100 year return period flood.  The 1:100 year flood refers to a flood that has a one percent chance of being equaled or exceeded in any one year.  It does not mean that it only occurs once every one 100 years or that once it occurs, an area is safe from it occurring for 100 years.  Each year has the same probability of a 1:100 year flood (1%).  Similarly, a 1:500 year return period flood is the flood that has a 0.2 percent chance of being equaled or exceeded in any one year.

# education

If the public understands their risk from flooding, then they will be able to take appropriate individual action in response to flood warnings.  These actions, coordinated with those of their neighbours and the rest of the community, will reduce flood damages and reduce the risk of loss of life.

The availability of flood hazard information increases the awareness of flood issues in a community.  Open houses on designation days and at other times offer opportunities for the public to learn about flood hazards in their communities.  By keeping individuals fully informed on these issues, the various levels of government can expect a better response from members of the public in the event of a flood.  Alberta Environment will continue to provide support to local governments after designation on flooding issues.

Flood hazard maps and other information are available on the Alberta Environment website at http://www3.gov.ab.ca/env/water/flood/index.html.  Visitors can either zoom in on an area of interest to see what information is available, or chose a community from the drop down menu.  At a scale of 1:20,000 or larger, the design flood elevations are visible; and at a scale of 1:10,000 or larger, the lot lines are visible.  Figure 3 shows a sample screen at a scale of 1:10,000 showing both the design flood elevations and the lot lines.   There is also an e-mail contact for further questions.

Figure 3:  Sample screen shot from the Flood Risk Map Information website.

# Conclusions

The Flood Hazard Identification Program was designed to assist Alberta municipalities to plan for appropriate development in their jurisdictions.  Alberta Environment supervises the production of the maps and sets standards.  The Flood Hazard Identification Program acts to:

- identify flood prone areas and minimize the risks and costs associated with flooding;

- provide guidelines for the use/non-use of flood prone lands; and

- increase public awareness of the flood hazard in their communities.

When the flood hazard maps are used appropriately in a community, the effect will be increased personal safety and reduced property damages. This will result in safer communities.

# References

Alberta Infrastructure.  2001. Flood Risk Management Guidelines for Location of New Facilities Funded by Alberta Infrastructure, Edmonton.  Document available on the internet at :http://www.infratrans.gov.ab.ca/INFTRA_Content/docType486/Production/FloodRiskMgmt.pdf

Canada- Alberta Flood Damage Reduction Program.  1989.  Canada-Alberta Flood Damage Reduction Program, Alberta Environmental Protection, Edmonton.